## Slide 1
RISP WORKSHOP 6
AUTONOMY LAYER
Practical Approach
From sensing to decision — making robots act automatically.
Autonomy
Fundamentals
FSM
Concepts
FSM
Exercise
Tinkercad
Impl.
ROS2
Intro
Bridge to
Intelligence

## Slide 2
WORKSHOP AGENDA
01
Autonomy Fundamentals
How robots sense, decide, and act
02
FSM Concepts
States, transitions, and behavior
03
FSM Exercise
Design your own FSM
04
Tinkercad Implementation
Read → Decide → Execute in code
05
ROS2 Introduction
Nodes, topics, live in your VM
06
Bridge to Intelligence
Autonomy reacts, AI understands

## Slide 3
01
AUTONOMY FUNDAMENTALS
How do robots decide what to do next?

## Slide 4
01
WHAT IS AUTONOMY?
Autonomy is the ability of a robot to make decisions and act without human input.
SENSE
Gather data from the environment using sensors — ultrasonic, IR, camera, IMU, GPS.
DECIDE
Process sensor data with a decision algorithm — FSM, PID, behavior tree, neural net.
ACT
Send commands to actuators — motors, servos, grippers — to affect the environment.
This loop runs continuously — hundreds of times per second in real systems. Speed and reliability of each stage determines robot performance.

## Slide 5
01
THE AUTONOMY FEEDBACK LOOP
SENSORS
Ultrasonic
Camera / IMU
GPS / LIDAR
PERCEPTION
Filter noise
Extract features
Map build
DECISION
FSM / Planner
Behavior tree
Algorithm
CONTROL
PID loop
Direct command
Safety check
ACTUATORS
Motors / ESCs
Servos
Grippers
FEEDBACK: Actuator output changes the environment — sensors pick it up again next cycle
REAL-WORLD EXAMPLES
IF Obstacle at 18 cm
→ STOP + back up
IF Path clear
→ MOVE FORWARD
IF Left blocked
→ TURN RIGHT
IF Person detected
→ SLOW + greet

## Slide 6
02
FINITE STATE MACHINES
Giving robots memory and structure

## Slide 7
02
WHAT IS AN FSM — AND WHY USE ONE?
WHAT IS AN FSM?
A Finite State Machine is a model of computation that:
• Has a finite number of states
• Is always in exactly ONE state at a time
• Transitions between states based on inputs
• Produces outputs based on current state
It is one of the oldest and most reliable tools in embedded and robotics programming.
WHY USE AN FSM?
Predictable
Every behavior is explicitly defined — no surprises or undefined states.
Debuggable
You always know which state the robot is in at any moment.
Scalable
Add new states without breaking existing ones.
Efficient
Runs fast — just comparisons and variable assignments.
Universal
Works on Arduino, PIC, FPGA, ROS — any platform.

## Slide 8
02
FSM: STATES & TRANSITIONS
ROBOT STATES
MOVE_FORWARD
Drive straight ahead at full speed
TURN_LEFT
Rotate left until obstacle is cleared
TURN_RIGHT
Rotate right until obstacle is cleared
STOP
Halt all motors — safety state
TRANSITION RULES
P1
IF front < 20 cm
→ STOP
P2
IF left < 15 cm
→ TURN_RIGHT
P3
IF right < 15 cm
→ TURN_LEFT
P4
IF all sensors clear
→ MOVE_FORWARD

## Slide 9
02
FSM STATE DIAGRAM
Each circle is a state. Each arrow is a transition triggered by a sensor condition.
MOVE
FORWARD
TURN
LEFT
TURN
RIGHT
STOP
front < 20
right < 15
left < 15
clear
clear
front > 30
MOVE_FORWARD TURN_LEFT TURN_RIGHT STOP

## Slide 10
03
FSM EXERCISE
Design your own state machine — time to think

## Slide 11
03
YOUR CHALLENGE: 3-SENSOR FSM DESIGN
Design a complete FSM for a robot with FRONT, LEFT, and RIGHT ultrasonic sensors. Define every state and every transition.
FRONT Sensor
Threshold: 20 cm
Detects obstacles directly ahead.
Highest priority — triggers STOP.
LEFT Sensor
Threshold: 15 cm
Detects walls on the left side.
Triggers TURN_RIGHT.
RIGHT Sensor
Threshold: 15 cm
Detects walls on the right.
Triggers TURN_LEFT.
DESIGN PROCESS
1
List all states
What distinct behaviors can your robot have?
2
Define transitions
For each state, what sensor values cause a change?
3
Draw the diagram
Circles = states. Arrows = transitions with labels.
4
Write the truth table
Map every sensor combination to an output state.

## Slide 12
04
TINKERCAD IMPLEMENTATION
Turning your FSM into real working code

## Slide 13
04
STEP 1 — READ YOUR SENSORS
Before your robot can decide anything, it needs to know what is around it.
sensor_read.ino
// Simulated reads (Tinkercad)
int front = readFront();
int left = readLeft();
int right = readRight();
// Real HC-SR04 ultrasonic
long dur = pulseIn(echoPin, HIGH);
int dist = dur * 0.034 / 2;
HOW HC-SR04 WORKS
1. Trigger pin sends 10 microsecond pulse
2. Sound wave travels out at 340 m/s
3. Echo pin goes HIGH when pulse returns
4. pulseIn() measures time in microseconds
5. Distance = time x speed / 2 (round trip)
KEY CONCEPTS
Noise filtering
Average 3-5 readings to remove false spikes
Update rate
Read every 20-50ms for smooth control
Deadband
Ignore tiny changes (<2cm) to avoid jitter

## Slide 14
04
STEP 2 — DEFINE YOUR STATES
states.ino
// All possible robot behaviors
enum State {
MOVE_FORWARD,
TURN_LEFT,
TURN_RIGHT,
STOP
};
// Starts moving forward
State currentState = MOVE_FORWARD;
WHY USE ENUM?
Using enum instead of raw integers:
• Makes code self-documenting
• Prevents invalid state values
• Enables switch/case cleanly
• Works on all Arduino boards
Internally it is just 0, 1, 2, 3 — but your code reads like English.
STATE
VALUE
DESCRIPTION
MOVE_FORWARD
0
Default — robot drives straight at set speed
TURN_LEFT
1
Left motors reverse, right motors forward
TURN_RIGHT
2
Right motors reverse, left motors forward
STOP
3
All motors off — highest safety priority

## Slide 15
04
STEP 3 — DECISION LOGIC
decision.ino
void updateState(int front, int left, int right) {
// SAFETY first — checked in priority order
if (front < 20) {
currentState = STOP;
}
else if (left < 15) {
currentState = TURN_RIGHT;
}
else if (right < 15) {
currentState = TURN_LEFT;
}
else {
currentState = MOVE_FORWARD;
}
}
Priority order matters
STOP is checked FIRST. The order of if/else determines which behavior wins when multiple sensors trigger.
Thresholds are tunable
20 cm and 15 cm are starting points. Calibrate based on your robot speed and sensor response time.
Hysteresis is critical
If threshold is 20 cm, only switch back to MOVE_FORWARD when dist > 30 cm. Prevents rapid state flipping.
Wrap in a function
Separating decision logic from execution makes code cleaner and easier to test independently.

## Slide 16
04
STEP 4 — EXECUTE BEHAVIOR
execute.ino
void executeBehavior() {
switch (currentState) {
case MOVE_FORWARD: moveForward(); break;
case TURN_LEFT: turnLeft(); break;
case TURN_RIGHT: turnRight(); break;
case STOP: stopMotors(); break;
}
}
loop.ino
void loop() {
updateState(front, left, right);
executeBehavior();
delay(30); // ~33 Hz update rate
}
MOTOR FUNCTIONS
moveForward()
Both motors forward at full duty cycle
turnLeft()
Left motor reverse, right motor forward
turnRight()
Right motor reverse, left motor forward
stopMotors()
Both motors zero — brake mode
delay(30) = 33 updates/sec. Too fast = sensor noise. Too slow = sluggish. 20-50ms is the sweet spot.

## Slide 17
05
ROS2 INTRODUCTION
The operating system of modern robotics

## Slide 18
05
WHAT IS ROS2?
ROS2 is a middleware framework for building modular, distributed robot software systems.
CORE CONCEPTS
Node: A single-purpose process
Topic: A named communication channel
Message: Data structure sent over a topic
Publisher: Node that sends messages to a topic
Subscriber: Node that receives from a topic
Executor: Manages callbacks and event loop
ROS2 vs ROS1
Feature
ROS1
ROS2
Master
roscore required
No master (DDS)
Real-time
Not supported
Full RT support
Security
None by default
SROS2 built-in
Python
Limited
Full rclpy
Lifecycle
Manual
Managed nodes

## Slide 19
05
ROS2 NODE ARCHITECTURE — WHAT WE BUILT
Two nodes. One topic between them. The FSM drives the robot directly via /cmd_vel.
Sensor Node
sensor_node.py
subscribes ← /scan (LaserScan)
publishes → /sensor_data (String JSON)
Reads Turtlebot3 LIDAR via /scan. Extracts front, left, right distances in cm. Publishes as JSON to /sensor_data.
/sensor_data
FSM Node
fsm_node.py
subscribes ← /sensor_data (String JSON)
publishes → /cmd_vel (Twist)
publishes → /fsm_state (String)
Runs the FSM. Picks state based on distances. Sends Twist velocity commands directly to the robot.
/cmd_vel → Turtlebot3 moves
MONITOR IN TERMINAL
ros2 topic echo /sensor_data
ros2 topic echo /fsm_state
ros2 topic echo /cmd_vel
ros2 node list

## Slide 20
05
ROS2 — ACTUAL CODE IN YOUR VM
sensor_node.py
class SensorNode(Node):
def __init__(self):
super().__init__('sensor_node')
self.scan_sub = self.create_subscription(
LaserScan, '/scan',
self.scan_callback, 10)
self.sensor_pub = self.create_publisher(
String, '/sensor_data', 10)
def scan_callback(self, msg):
front = get_valid_range(msg.ranges, 0)
left = get_valid_range(msg.ranges, 90)
right = get_valid_range(msg.ranges, 270)
data = {'front_cm': front*100,
'left_cm': left*100,
'right_cm': right*100}
out = String()
out.data = json.dumps(data)
self.sensor_pub.publish(out)
fsm_node.py
class FSMNode(Node):
def __init__(self):
super().__init__('fsm_node')
self.sub = self.create_subscription(
String, '/sensor_data',
self.sensor_callback, 10)
self.cmd_pub = self.create_publisher(
Twist, '/cmd_vel', 10)
def sensor_callback(self, msg):
data = json.loads(msg.data)
self.update_state(
data['front_cm'],
data['left_cm'],
data['right_cm'])
self.execute_behaviour()
RUN IN YOUR VM — 3 terminals
$ ros2 run risp_autonomy sensor_node
$ ros2 run risp_autonomy fsm_node
$ ros2 topic echo /fsm_state

## Slide 21
06
BRIDGE TO INTELLIGENCE
Autonomy reacts. Intelligence understands.

## Slide 22
06
AUTONOMY vs INTELLIGENCE
Both stop the robot — but for very different reasons.
BEFORE — AUTONOMY (Reactive)
reactive.ino
if (distance < 20)
stop();
// that's all it knows.
What the robot knows:
X Something is 18 cm away
X Not what it is
X Not if it is moving
X Not if it is dangerous
AFTER — INTELLIGENCE (Context)
intelligent.py
if personDetected():
stop()
greet() # context-aware!
What the robot knows:
OK It is a person, not a wall
OK They are standing still
OK It is safe to approach
OK Appropriate action: greet

## Slide 23
06
THE FULL ROBOTICS INTELLIGENCE STACK
Your FSM is the foundation. Here is what gets built on top of it.
LAYER 5
Mission Planning
High-level goals — go to room B, pick up object. Decomposes into sub-tasks.
LAYER 4
Path Planning
A*, RRT, Dijkstra — find a route through a map without hitting obstacles.
LAYER 3
Perception
Computer vision, SLAM, object detection — building a model of the world.
LAYER 2
Behavior (FSM/BT)
YOU ARE HERE. States, transitions, reactive behavior. Core of this workshop.
← YOU ARE HERE
LAYER 1
Hardware Drivers
Sensor reads, motor PWM, serial comms — direct hardware interface.

## Slide 24
WORKSHOP COMPLETE
RISP Workshop 6 — Autonomy Layer
Autonomy Fundamentals
Sense → Decide → Act. The core feedback loop that drives all autonomous robots.
FSM Concepts & Diagram
States, transitions, priorities. Predictable and debuggable robot behavior.
FSM Exercise
You designed a 3-sensor FSM from scratch — states, transitions, truth table.
Tinkercad Code
Read → updateState() → executeBehavior(). Clean separation of concerns.
ROS2 Nodes and Topics
Sensor node publishes, FSM node subscribes, control node acts. Live in VM.
Bridge to Intelligence
FSM reacts to numbers. AI understands context. Layer 2 of the full stack.